## Slide 1
Deep Reinforcement Learning for Dynamic Task Offloading in the 5G Edge-Cloud Continuum
Final term paper presentation | Mobile Communications and Cloud Computing
Presented by: Syahril Fahmi
Southern Taiwan University of Science and Technology
Instructor: Dr. Showkat Ahmad Bhat
5G
MEC
Cloud
Notes: Introduce yourself and the paper. One sentence: this paper teaches each IoT device to decide, on its own, whether to run a task locally, at the 5G edge server (MEC), or in the cloud, using deep reinforcement learning.

## Slide 2
Roadmap
Nieto et al., J. Cloud Computing 13, 94 (2024)
2
1
Paper overview and motivation
2
Problem and research gap
3
System model: network, tasks, latency, energy
4
DRL formulation and Actor-Critic algorithm
5
Experiments and results
6
Critical analysis, course relevance, conclusion
Notes: Quick overview of the talk. About 15-20 minutes: motivation, method, results, critique.

## Slide 3
The paper at a glance
Nieto et al., J. Cloud Computing 13, 94 (2024)
3
Title
Deep Reinforcement Learning techniques for dynamic task offloading in the 5G edge-cloud continuum
Authors
G. Nieto, I. de la Iglesia, U. Lopez-Novoa, C. Perfecto
Journal
Journal of Cloud Computing (Springer), vol. 13, art. 94
Published
3 May 2024
DOI
10.1186/s13677-024-00658-0
In one sentence
Each 5G device runs its own Actor-Critic agent that learns where to execute every task (local, MEC or cloud) to save battery while meeting the deadline.
Notes: Give the citation. Journal of Cloud Computing is a Springer open-access journal; the paper was published online 3 May 2024, so it is within the last three years.

## Slide 4
Motivation: why offloading is hard
Nieto et al., J. Cloud Computing 13, 94 (2024)
4
1
Constrained devices
IoT and mobile devices have limited CPU and battery, so heavy tasks cannot always run locally.
2
Cloud is far
Cloud computing has huge capacity, but the round trip is too slow for latency-critical tasks.
3
Edge is close but small
Multi-access Edge Computing (MEC) sits at the base station: low delay, limited resources.
4
Conditions keep changing
Channel quality, server load and battery level vary, so one fixed rule cannot stay optimal.
Notes: IoT devices have limited CPU and battery. Cloud has huge capacity but is far away. MEC is close but small. The best choice changes over time, so a fixed rule fails.

## Slide 5
Problem statement and research gap
Nieto et al., J. Cloud Computing 13, 94 (2024)
5
Goal: for every task, choose local, MEC or cloud execution to maximize QoE (energy saved) while meeting the latency deadline.
Heuristics / metaheuristics
Do not adapt to dynamic conditions; centralized versions scale poorly; some ignore battery and channel status.
Centralized ML
Network overhead and privacy concerns; many ignore the cloud tier or use one task type.
This paper
Distributed: one agent per device. Three task classes, three execution options, dynamic network and server behavior.
Notes: The authors argue that heuristics do not adapt, centralized ML creates overhead and privacy issues, and many ML papers ignore the cloud or multiple task classes. Their claim is that theirs is the only distributed ML approach with several task classes.

## Slide 6
Key contributions
Nieto et al., J. Cloud Computing 13, 94 (2024)
6
1
A system model that captures device and server occupancy, network status and several task types
2
A QoE metric based on energy use, conditioned on meeting the latency requirement
3
A distributed DRL approach: adaptive offloading decisions for each device in a time-varying environment
4
Experiments showing dynamic approaches are necessary and that the proposal beats the baselines
Notes: Read the four contributions. Emphasize the second and third as the technical core.

## Slide 7
System architecture: three tiers
Nieto et al., J. Cloud Computing 13, 94 (2024)
7
User Equipment
Battery, CPU 1.5 GHz
α = 0: run locally
Base station + MEC
MEC
10 GHz
α = 1: offload to edge
Cloud
50 GHz
α = 2: offload to cloud
Wireless link
30-150 m
Optical fiber
50 km, 10 Tbps
Notes: Explain the three options for each task. Devices connect wirelessly to a base station that hosts the MEC server; the cloud is reached through the base station over optical fiber. The UE to MEC distance is treated as the UE to BS distance.

## Slide 8
Task model: three task classes
Nieto et al., J. Cloud Computing 13, 94 (2024)
8
1
Class 1: delay-sensitive
Smart sensors. Deadline 10-50 ms
2
Class 2: energy-sensitive
AR applications. Deadline 50-500 ms
3
Class 3: insensitive
Smart-grid analytics. Deadline 0.5-2 s
Chart: Maximum data size per task (KB)
| Class 1 | Class 2 | Class 3
Max data size (KB) | 100 | 500 | 2000
Notes: Each task has data size D, required CPU cycles phi, and a deadline. Class 1 is delay sensitive (sensors), Class 2 is energy sensitive (AR), Class 3 is insensitive (smart-grid analytics). The chart shows the maximum data size per class from Table 3 of the paper.

## Slide 9
Latency and energy models
Nieto et al., J. Cloud Computing 13, 94 (2024)
9
Local
Latency: t = φ / f
Energy: e = κ · f² · φ
MEC
Latency: t = D / R + φ / f_MEC
Energy: e = p · D / R
Cloud
Latency: t = D / R + fiber delay + φ / f_cloud
Energy: e = p · D / R (same as MEC)
R = W · log₂(1 + p·h / N₀) is the uplink rate; channel gain h follows the 3GPP TR 38.901 indoor model (path loss + 5.9 dB shadow fading).
Notes: Explain the structure rather than reading formulas. Local latency is cycles over CPU speed. Offloading adds wireless transmission using Shannon capacity plus remote processing; the cloud path adds fiber transmission and propagation. Local energy grows with the square of CPU frequency. Offloading energy is only the transmission energy, which is why MEC and cloud cost the same battery.

## Slide 10
DRL formulation: state, action, reward
Nieto et al., J. Cloud Computing 13, 94 (2024)
10
State (6 values)
Battery level
UE free resources
MEC free resources
Cloud free resources
Channel gain
Task class
Action (3 choices)
0 = execute locally
1 = offload to MEC
2 = offload to cloud
Reward = QoE
Deadline met: −energy used ÷ battery capacity
Deadline missed: penalty η = −100
Objective: maximize the sum of QoE over all time steps, subject to resource constraints. Agents are non-cooperative: no central controller.
Notes: Each device is an independent, non-cooperative agent. State has six elements; action has three choices; reward is negative energy as a fraction of the battery if the deadline is met, and a fixed penalty of minus 100 if it is missed.

## Slide 11
Actor-Critic agent on every device
Nieto et al., J. Cloud Computing 13, 94 (2024)
11
2 × 256
hidden neurons in each network
10⁻⁵ / 10⁻⁴
learning rate: actor / critic
γ = 0.99
discount factor, Adam optimizer
Actor
State → TanH layers → softmax over {local, MEC, cloud}. Picks the offloading action.
Critic
State → TanH layers → linear value. Its temporal-difference (TD) error updates the actor and the critic.
Notes: Two separate networks: the actor outputs a probability for each of the three actions using softmax; the critic estimates state value and gives a temporal-difference signal to train the actor. The authors compare separated networks against shared hidden layers.

## Slide 12
Experimental setup
Nieto et al., J. Cloud Computing 13, 94 (2024)
12
Simulator
Python 3.10, TensorFlow 2.14, Gymnasium 0.29
Topology
1 cloud server, 1 MEC server at the BS, multiple UEs
UE battery
10,000 mJ
UE transmit power
200 mW; noise −80 dBm
Distances
UE-BS 30-150 m; BS-cloud 50 km
QoE penalty
η = −100 for a missed deadline
Chart: Compute capacity (GHz)
| UE | MEC | Cloud
Compute (GHz) | 1.5 | 10 | 50
Notes: Simulation built in Python with TensorFlow and Gymnasium. Key parameters are in the list. The chart shows how much compute each tier has, which explains why cloud is not always best: distance and deadline matter.

## Slide 13
Evaluation scenarios and baselines
Nieto et al., J. Cloud Computing 13, 94 (2024)
13
Scenario 1: MEC outages
MEC unavailable at steps 500-750 and 1250-1500. Tested with 90% Class 1, 90% Class 2, 90% Class 3, and a mixed workload.
Scenario 2: communication failure
MEC stays available (80-100% capacity) but the wireless link fails during steps 500-1000, so nothing can be offloaded.
Static baselines
Always Local, always MEC, always Cloud
Dynamic methods
Random, Joint-Networks AC, Double Dueling DQN, and the proposed Separated-Networks AC
Notes: Two stress tests. In scenario 1 the MEC goes offline for two periods. In scenario 2 the wireless link fails between steps 500 and 1000. Baselines are three fixed policies and three dynamic ones.

## Slide 14
Results: scenario 1 (MEC outages)
Nieto et al., J. Cloud Computing 13, 94 (2024)
14
Workload | Static baselines | Separated-Networks AC (proposed)
90% Class 1 (delay) | Cloud worst (misses deadlines); Local drains battery; MEC best while available | Best dynamic method; switches after MEC fails
90% Class 2 (energy) | Local worst; MEC and Cloud use similar battery | Slightly better than Joint-Networks AC
90% Class 3 (insensitive) | Local worst; MEC and Cloud QoE near 0 | Keeps more battery; uses MEC, then cloud during outages
Mixed | MEC is the best static choice | Best QoE overall; DDDQN worst on battery and QoE
DDDQN = Double Dueling Deep Q-Network. It learned more slowly than the Actor-Critic variants in the reported runs.
Notes: The paper reports these mostly as QoE and battery curves, so I summarize the qualitative outcome per workload. The key point: the fixed policies each win in one situation and fail in another, while the proposed agent adapts.

## Slide 15
Results: scenario 2 and key findings
Nieto et al., J. Cloud Computing 13, 94 (2024)
15
No fixed policy wins
Cloud fails delay-critical tasks, Local drains the battery on heavy tasks, MEC fails when the edge is down.
Agents adapt online
The proposed agents use MEC as long as it is up, then move to cloud or local when it is not.
Separated networks help
Separate actor and critic gave slightly better results than shared hidden layers.
Link failure handled
When the wireless link fails, dynamic agents adjust and outperform static baselines.
Notes: Scenario 2 is qualitative in the paper: the agents change strategy when the link fails. Summarize the four takeaways.

## Slide 16
Critical analysis
Nieto et al., J. Cloud Computing 13, 94 (2024)
16
Strengths
Distributed: no central controller, lower overhead and better privacy
Three execution options and three task classes
Tests failure cases, not only the normal case
Physically grounded model (3GPP channel, fiber link)
Limitations
Tasks cannot be split; no partial offloading or dependencies
Simple FIFO queues; fast fading averaged out
Scalability with many agents not tested
Simulation only, two scenarios, no real testbed
Notes: Strengths and limitations. Be clear these are my own assessments plus the limitations the authors acknowledge. Notably, results are simulation-only and reported mostly as curves.

## Slide 17
Relevance to our course and future work
Nieto et al., J. Cloud Computing 13, 94 (2024)
17
Link to the course
Mobile communications: 5G wireless link, Shannon rate, path loss, shadow fading
Cloud computing: MEC and cloud tiers, resource occupancy, latency
Shows why the edge-cloud continuum exists
Future directions
More complex environments and task types
Many more UEs to test scalability
Cloud-edge-device collaboration
Task dependencies and partial offloading
Notes: Connect back to the course: 5G radio links and channel models are mobile communications; MEC and cloud servers are cloud computing. The paper sits exactly at their intersection.

## Slide 18
Conclusion
Fixed offloading rules break when the network and server load change.
A distributed Actor-Critic agent per device learns to choose local, MEC or cloud from six observed values.
It achieves the best QoE and battery use among the compared methods in the simulated failure scenarios.
Thank you. Questions?
Notes: Summarize in three sentences and invite questions. Possible questions: why Actor-Critic instead of DQN? (the paper found AC learned faster than DDDQN here); why does cloud cost the same battery as MEC? (fiber adds no UE energy); what if there are many UEs? (not tested, listed as future work).